## Slide 1
Typical Applications
Test Instrumentation
Microwave Radio & VSAT
Military & Space
Telecom Infrastructure
Fiber Optics
Features
Frequency: 45-90GHz
Small Signal Gain: 15dB Typical
Gain Flatness: ±2.5dB Typical
Noise Figure:4.5dB Typical
P1dB: 12dBm Typical
Power Supply:
VD=+4V@119mA ,VG=-0.4V
Input/Output: 50Ω
Chip Size: 1.766 x 2.0 x 0.05mm
Parameters | Min. | Typ. | Max. | Min. | Typ. | Max. | Units
Frequency | 45-70 |  |  | 70-90 |  |  | GHz
Small Signal Gain | 14 | 14.5 |  | 16 | 18 |  | dB
Gain Flatness |  | ±1.0 |  |  | ±1.0 |  | dB
Noise Figure |  | 4.5 |  |  | 6.5 |  | dB
P1dB - Output 1dB Compression |  | 12 |  |  | 14 |  | dBm
Psat - Saturated Output Power |  | 15 |  |  | 18 |  | dBm
OIP3 - Output Third Order Intercept |  | 20 |  |  | 22 |  | dBm
Input Return Loss |  | -18 |  |  | -13 |  | dB
Output Return Loss |  | -13 |  |  | -18 |  | dB
Electrical Specifications
TA = +25⁰C, VD = +4V , VG=-0.4V , IDD = 119mA Typical
Functional Block Diagram

## Slide 2
Measurement Plots: S-parameters
VD=4.0V,VG=-0.5V
Measurement Plots: S-parameters
TA = +25⁰C

## Slide 3
Measurement Plots: P1dB
TA = +25⁰C
Measurement Plots: OIP3
TA = +25⁰C
Measurement Plots: PSAT
TA = +25⁰C
Measurement Plots: Noise Figure
TA = +25⁰C

## Slide 4
Measurement Plots: S-parameters
VD=3.5V,VG=-0.38V
Measurement Plots: S-parameters
VD=4V,VG=-0.4V

## Slide 5
Measurement Plots: P1dB
VD=3.5V,VG=-0.38V
Measurement Plots: P1dB
VD=4V,VG=-0.4V
Measurement Plots: OIP3
VD=3.5V,VG=-0.38V
Measurement Plots: OIP3
VD=4V,VG=-0.4V

## Slide 6
Measurement Plots: PSAT
VD=3.5V,VG=-0.38V
Measurement Plots: PSAT
VD=4V,VG=-0.4V
Measurement Plots: Noise Figure
VD=3.5V,VG=-0.38V
Measurement Plots: Noise Figure
VD=4V,VG=-0.4V

## Slide 7
Drain Bias Voltage (VD) | +4.5V
Gate Bias Voltage (VG) | -2V to 0V
RF Input Power (RFIN)@(+4V) | +15dBm
Channel Temperature | 175°C
Continuous Pdiss (T = 85 °C) (derate 6.1mW/°C above 85 °C) | 0.55W
Thermal Resistance (channel to die bottom) | 50°C/W
Operating Temperature | -55°C to +85 °C
Storage Temperature | -65°C to +150 °C
Absolute Maximum Ratings
VD (V) | VG (V) | IDD (mA)
+3.5 | -0.38 | 118
+4.0 | -0.40 | 119
+4.0 | -0.50 | 71
Typical Supply Current vs. VD,VG
ELECTROSTATIC SENSITIVE DEVICE OBSERVE HANDLING PRECAUTIONS

## Slide 8
Outline Drawing:
All Dimensions in μm
Notes: 1. Die thickness: 50μm 2. VD bond pad is 75*75μm2 3. VG bond pad is 75*75μm2 4. RF IN/OUT bond pad is 50*86μm2 5. Bond pad metalization: Gold 6. Backside metalization: Gold

## Slide 9
Assembly Drawing
No | Function | Description
1 | RF IN | RF signal input terminal; no blocking capacitor required.
2 | RF OUT | RF signal output terminal; no blocking capacitor required.
3 | VD | Drain Biases for the Amplifier ; An external biasing circuit is required.
4 | VG | Gate Biases for the Amplifier ; An external biasing circuit is required.
5 | Die Bottom | Die bottom must be connected to RF and dc ground.
Item | Description
C1 | 100pF Example: Skyworks Part: SC10002430
C2 | 0.01µF Example: TDK Part:C1005X7R1H103K050BB (0402)
C3 | 0.1µF Example: TDK Part:C1005X7R1H104K050BB (0402)
R1 | 10Ω Example: Yageo Part:SR0402FR-7T10RL

## Slide 10
Biasing and Operation
Turn ON procedure:
Connect GND to RF and dc ground.
Set the gate bias voltages,VG to −2V.
Set the drain bias voltages VD to +4V .
Increase the gate bias voltages to achieve a quiescent supply current of 82 mA.、
Apply RF signal.
Turn OFF procedure:
Turn off the RF signal.
Decrease the gate bias voltages, VG to −2V to achieve a IDQ = 0 mA (approximately).
Decrease the drain bias voltages to 0 V.
Increase the all gate bias voltages to 0 V.

## Slide 11
Miller MMIC Inc. All rights reserved
Miller MMIC, Inc. holds exclusive rights to the information presented in its Data Sheet and any accompanying materials. As a premier supplier of cutting-edge RF solutions, Miller MMIC has made this information easily accessible to its clients.
Although Miller MMIC believes the information provided in its Data Sheet to be trustworthy, the company does not offer any guarantees as to its accuracy. Therefore, Miller MMIC bears no responsibility for the use of this information. It is worth mentioning that the information within the Data Sheet may be altered without prior notification.
Customers are encouraged to obtain and verify the most recent and pertinent information before placing any orders for Miller MMIC products. The information in the Data Sheet does not confer, either explicitly or implicitly, any rights or licenses with regards to patents or other forms of intellectual property to any third party.
The information provided in the Data Sheet, or its utilization, does not bestow any patent rights, licenses, or other forms of intellectual property rights to any individual or entity, whether in regards to the information itself or anything described by such information. Furthermore, Miller MMIC products are not intended for use as critical components in applications where failure could result in severe injury or death, such as medical or life-saving equipment, or life-sustaining applications, or in any situation where failure could cause serious personal injury or death.
Mounting & Bonding Technigues for MMICs
Direct Mounting
1.Typically, the die is mounted directly on the ground plane.
2.If the thickness difference between the substrate (thickness c) and the die (thickness d) exceeds 0.05 mm (i.e., c – d > 0.05 mm), it is recommended to first mount the die on a heat spreader, then attach the heat spreader to the ground plane.
3.Heat Spreader Material: Molybdenum-copper (MoCu) alloy is commonly used.
4.Heat Sink Thickness (b): Should be within the range of (c – d – 0.05 mm) to (c – d + 0.05 mm).
5.Spacing (a): The gap between the bare die and the 50Ω transmission line should typically be 0.05 mm to 0.1 mm.
If the application frequency is higher than 40GHz, then this gap is recommended to be 0.05mm
Wire Bonding Interconnection
The connection between the die and the 50Ω transmission line is usually made using 25 µm diameter gold (Au) wires, bonded via wedge bonding or ball bonding processes.
Die Attachment Methods
1.Conductive Epoxy:
After adhesive application, cure according to the manufacturer’s recommended temperature profile.
2.Au-Sn80/20 Eutectic Bonding:
Use preformed Au-Sn80/20 solder preforms.
Perform bonding in an inert atmosphere (N₂ or forming gas: 90% N₂ + 10% H₂).
Keep the time above 320°C to less than 20 seconds to prevent excessive intermetallic formation.